## Slide 1: Traversability and Mapping of Obstacles in Uneven Terrain Based on a Robot’s Design
Bachelor Thesis by Max-Ole von Waldow
Supervised by Dr. Ngoc Thinh Nguyen and Prof. Dr. Georg Schildbach
Notes: Welcome to colloquium
Title of my Bachelor thesis is …

## Slide 2: Table of Contents
Motivation and Background
Contributions
  Terrain Features and Traversability
  Implementation Approaches
Evaluation and Comparisons
Conclusions and Future Work
Notes: Start out with …
Go into …
Look at …
Talk about …
Cover …
discuss …
Evaluate & Compare
Finish with …

## Slide 3: Motivation
Use cases:
  Agriculture (KRIBL project)
  Extraterrestrial exploration
  Rescue robotics
Goals
  Determine traversability tailored to design of the robot
  Map obstacles for navigation software
  Modularity
  Expand projects to rough terrain
Motivation and Background
Notes: Use-cases with Need for navigation in uneven terrain
Ongoing KRIBL project involving ROB institute: move through crop fields
Space: not structured environment to drive in. Rover on mars stuck  expensive mission fail, nobody there to physically fix situation
Rescue robotics: man-made structures destroyed after disaster. Navigate in ruins to aid victims & emergency forces
 In common: robotic platform need to traverse unstructured environments safely
Determine traversability in uneven terrain  tailored to specific robot -> bc robot specification affects traversability
Save Untraversable regions as obstacles in map  3rd party software
Embrace modularity. Want to make our method easy integrate.
Expand … work in …

## Slide 4: Background
Jackal [Chen, 2017]
ZED Camera [Ortiz, 2018]
Motivation and Background
[Chen, 2017]
Chen, Y. F., Everett, M., Liu, M., and How, J. P. Socially aware motion planning with deep reinforcement learning. In: 2017 IEEE/RSJ International Conference on Intelligent Robots and Systems (IROS). IEEE. 2017, pp. 1343–1350.
[Ortiz, 2018]
Ortiz, L. E., Cabrera, V. E., and Goncalves, L. M. Depth data error modeling of the ZED 3D vision sensor from stereolabs. In: ELCVIA: electronic letters on computer vision and image analysis 17(1):1–15, 2018.
Notes: Jackal:
Why: -> rugged, mobile platform  optimal
ZED Stereo camera:
Why: -> already equipped, detailed point cloud(for small edges), (visual odometry)

## Slide 5: Background
Jackal [Chen, 2017]
ZED Camera [Ortiz, 2018]
ROS [Quigley, 2009]
Motivation and Background
[Quigley, 2009]
Quigley, M., Conley, K., Gerkey, B., Faust, J., Foote, T., Leibs, J., Wheeler, R., Ng, A. Y., et al. ROS: an open-source Robot Operating System. In: ICRA workshop on open source software. Vol. 3. 3.2. Kobe, Japan. 2009, p. 5.
Notes: Why: -> modular, widespread, existing 3rd party packages

## Slide 6: Background
Jackal [Chen, 2017]
ZED Camera [Ortiz, 2018]
ROS [Quigley, 2009]
Elevation Mapping
[Fankhauser, 2018]
  Grid map [Fankhauser, 2016]
  Filter chain
Motivation and Background
[Fankhauser, 2018]
Fankhauser, P., Bloesch, M., and Hutter, M. Probabilistic Terrain Mapping for Mobile Robots with Uncertain Localization. In: IEEE Robotics and Automation Letters (RA-L) 3(4):3019–3026, 2018.
[Fankhauser, 2016]
Fankhauser, P. and Hutter, M. A Universal Grid Map Library: Implementation and Use Case for Rough Terrain Navigation. In: Robot Operating System (ROS) – The Complete Reference (Volume 1). Ed. by A. Koubaa. Springer, 2016. Chap. 5.
meters
Image from [Fankhauser, 2016]
Notes: Why:
-> robot-centric,
-> convenient data structure, multiple values per coordinate in the map
-> easy processing with filter chain

## Slide 7: Terrain Features and Traversability
Slopes
  Tipping
  Slipping
  Lack of motor power
Edges
Combination:
  Small edges inhibit obstacles from high slopes
Contributions
Subsumption architecture [Brooks, 1991]
[Brooks, 1991]
Brooks, R. A. New approaches to robotics. In: Science 253(5025):1227–1232, 1991.
Notes: Cannot anticipate all types of untraversable regions
Abstract feature to cover most
General properties:
- Slope (walls, hill, holes, …)
single variable: angle
failure cases: …
slope limit each  minimum
- Edges (sidewalk curb, small rock)
steep slope, consider height instead of inclination
Combine Features  Subsumption architecture
Regard Slope & Edge as behaviors; both have threshold (angle, edge height, respectively) to classify region traversable or not
- slope default
- exception: small edge inhibits region being marked as obstacle by slope behavior

## Slide 8: Subsumption architecture [Brooks, 1991]
Contributions
Merged Obstacles from slope and edge behaviors | Slope: obstacle | Slope: traversable
Edge: obstacle | Obstacle | Not Possible
Edge: traversable | No Obstacle | No Obstacle
[Brooks, 1991]
Brooks, R. A. New approaches to robotics. In: Science 253(5025):1227–1232, 1991.
Notes: Slope traversable  edge behavior not active. No steep slope means no edge
Both Obstacle  Both agree; Edge does not inhibit slope
Only slope obstacle  slope has false positive; Edge inhibits slope obstacle

## Slide 9: Slopes - Tipping
Forces
  Gravity
  Inertial force due to acceleration
Tipping starts at equilibrium of Moments
 Model:
Contributions
Notes: Red: CoG
Green: Critical tipping point, Hind contact points with ground
Static case (no accel): Gravity, slope angle effects len L, (lever arm of Force around tipping point)
Dynamic: Inertial force, tips robot accelerating uphill
( simplified, Forces act at contact points with ground. Mass resists acceleration  called inertia )
Both forces create moments around point marked green. Equilibrium

## Slide 10
Contributions
Video: Slope angle: 35°
Acceleration: 0.2
 Success
Notes: Experiment to Validate
Ramp leans on and is strapped to different levels of staircase railing

## Slide 11
Contributions
Video: Slope angle: 35°
Acceleration: 1.0
 Failure
Notes: ( Limit at deg : 0.9 m/s^2 )
( Slope limit at max accel (m/s^2): … deg )

## Slide 12: Slopes - Tipping
Find Center of Gravity (CoG)
  Balance Jackal above edge
  CoG must lie above edge in plane (orange)
  Define plane through angle with law of cosines (blue)
Contributions
Notes: CoG must lie above edge => orange

## Slide 13: Slopes - Tipping
Find Center of Gravity (CoG)
  Balance Jackal above edge
  CoG must lie above edge in plane (orange)
  Define plane through angle with law of cosines (blue)
  CoG =
Contributions
x
y
CoG
Notes: Result:
Frame base_link, geometric center
Top view, position exaggerated for visualization

## Slide 14: Slopes - Slipping
Skid steering increases slippage
Experiment to find inclination limit with tolerable slippage
Contributions
Notes: Jackal differentially driven, skid steering
Expect: higher slope <-> higher slippage

## Slide 15
Contributions
Video: Ramp inclination: 25°
Pre-programmed motion
 No correlation found
between angle and slippage
Notes: No correlation …
 won’t take slippage into account for Jackal

## Slide 16: Slopes - Lack of motor power
Wheel torque to overcome gravity
Calculate wheel torque from power etc.
Contributions
Notes: Robot needs enough wheel torque to overcome gravity.
Motors need to be powerful to move the robot’s own weight.
T = r*P/v
( 500 Watt drive power ) which is large enough to control Jackal on any inclination.

## Slide 17: Slopes - Lack of motor power
Wheel torque to overcome gravity
Calculate wheel torque from power and velocity
Contributions
Radius
Torque
Force
Driven Wheel
Notes: Robot needs enough wheel torque to overcome gravity.
Motors need to be powerful to move the robot’s own weight.
( 500 Watt drive power ) which is large enough to control Jackal on any inclination.
TODO fig?

## Slide 18: Edges
Experiment with variables:
  Edge height
  Approach angle
  Driving direction
Contributions
Notes: Vary: Edge height, Approach angle, (driving direction)
friction, wheel type of Jackal

## Slide 19
Contributions
Video: Edge height: 5 cm
Approach angle: 0°
Driving direction: Backwards
 Success

## Slide 20
Contributions
Video: Edge height: 5 cm
Approach angle: 45°
Driving direction: Forwards
 Failure
Notes: Approach angle has a major impact of what edge height can be traversed.
( Edge limit: 3.0 cm (regardless of approach angle & driving direction) )

## Slide 21: Edges
Experiment
Ground clearance
Contributions

## Slide 22: Edges
Experiment
Ground clearance
Footprint
Contributions
Notes: Footprint: 37.559 cm square

## Slide 23: Implementation Approachs – Conservative Method
Assume worst control
Output conservative obstacles
Contributions
Filter Chain
Control Software
Drive
Conservative Obstacles
Control
Output
Elevation mapping
Height
Map
Notes: configure filter chain in Compile Step, evaluate models
Control software includes path planner and controller to move robot along path
No feedback
can’t know how robot will move
Problem bc: traversability of slope depends on accel & edge height that can be overcome depends on approach angle
[CLICK] Can’t know variables, Assume worst control
[CLICK] conservative obstacles
Restrictive map

## Slide 24: Implementation Approachs – Control Limiting Method
Assume best control
Output control limits and fundamental obstacles
Contributions
Filter Chain
Control Software
Drive
Fundamental Obstacles
Control limiting
Control
Output
Limited
Control
Output
Elevation mapping
Height
Map
Control
Limits
Notes: Compile step: configure filter chain
Influence control limits
 [CLICK] assume best control
 [CLICK] Fundamental obstacles

## Slide 25: Filter Chain
Contributions
Slope
Behavior
Edge
Behavior
Combination
Notes: Elevation Mapping Package
Slope behavior
Edge behavior
Combination with Subsumption arbiter
Visualization, convert grid map layer to occupancy grid for which more tools exist

## Slide 26: Evaluation and Comparisons
Evaluation and Comparisons
Skate park
Notes: Why?: All Obstacle
(left) island; (back) double ramp; (between) our obstacles; types available

## Slide 27: Evaluation and Comparisons
Skate park
Software
  move_base controller
  Offline B-Spline path planner [Nguyen, 2021]
  gmapping [Grisetti, 2007]
Evaluation and Comparisons
[Nguyen, 2021]
Nguyen, N. T., Schilling, L., Angern, M. S., Hamann, H., Ernst, F., and Schildbach, G. B-spline path planner for safe navigation of mobile robots. In: 2021 IEEE/RSJ International Conference on Intelligent Robots and Systems (IROS). IEEE. 2021, pp. 339–345.
[Grisetti, 2007]
Grisetti, G., Stachniss, C., and Burgard, W. Improved techniques for grid mapping with rao-blackwellized particle filters. In: IEEE transactions on Robotics 23(1):34–46, 2007.
meters
Notes: Image our elevation mapping:
(left) island; (back) double ramp; (between) our obstacles; (front) sensor errors
Move base: Part of ROS navigation stack
B-Spline path planner: Offline, because no ROS integration
Gmapping: Standard, commonly used SLAM method for 2D cases

## Slide 28: Evaluation and Comparisons
Fundamental and conservative obstacles (overlayed)
  Fundamental obstacles are less exaggerated
Evaluation and Comparisons
Notes: Island top right, where difference is especially visible

## Slide 29: Evaluation and Comparisons
Fundamental and conservative obstacles (overlayed)
  Fundamental obstacles are less exaggerated
Integration with B-Spline path planner [Nguyen, 2021]
Evaluation and Comparisons
B-Spline in conservative map
[Nguyen, 2021]
Nguyen, N. T., Schilling, L., Angern, M. S., Hamann, H., Ernst, F., and Schildbach, G. B-spline path planner for safe navigation of mobile robots. In: 2021 IEEE/RSJ International Conference on Intelligent Robots and Systems (IROS). IEEE. 2021, pp. 339–345.
Notes: Map divided into polytopes
Asked find path around island

## Slide 30: Evaluation and Comparisons
Fundamental and conservative obstacles (overlayed)
  Fundamental obstacles are less exaggerated
Integration with B-Spline path planner [Nguyen, 2021]
Evaluation and Comparisons
B-Spline in non-conservative map
[Nguyen, 2021]
Nguyen, N. T., Schilling, L., Angern, M. S., Hamann, H., Ernst, F., and Schildbach, G. B-spline path planner for safe navigation of mobile robots. In: 2021 IEEE/RSJ International Conference on Intelligent Robots and Systems (IROS). IEEE. 2021, pp. 339–345.

## Slide 31: Evaluation and Comparisons
Fundamental and conservative obstacles (overlayed)
  Fundamental obstacles are less exaggerated
Integration with B-Spline path planner [Nguyen, 2021]
  Orange path is shorter and subject to control limits
Evaluation and Comparisons
control limit method
conservative method
[Nguyen, 2021]
Nguyen, N. T., Schilling, L., Angern, M. S., Hamann, H., Ernst, F., and Schildbach, G. B-spline path planner for safe navigation of mobile robots. In: 2021 IEEE/RSJ International Conference on Intelligent Robots and Systems (IROS). IEEE. 2021, pp. 339–345.

## Slide 32: Evaluation and Comparisons
Evaluation and Comparisons
Control limits on path
Safety margin

## Slide 33: Comparison with gmapping [Grisetti, 2007]
Evaluation and Comparisons
[Grisetti, 2007]
Grisetti, G., Stachniss, C., and Burgard, W. Improved techniques for grid mapping with rao-blackwellized particle filters. In: IEEE transactions on Robotics 23(1):34–46, 2007.
Notes: Ask move_base to find Similar Path around island in this map
Island not well represented in map  path planner chooses straight line
Leads Jackal on Dangerous path, not suited for uneven environments

## Slide 34: Comparison with gmapping [Grisetti, 2005 and 2007]
No traversability consideration
Issue with 2D sensor information
Evaluation and Comparisons

## Slide 35: Conclusions
Able to determine traversability
Outperforms gmapping in uneven terrain
Modular
  Pro: Easy to integrate
  Contra: Future trajectory unknown; Assumptions needed
  (mitigated by control limiting approach)
Future Work
Reduce assumptions
Consider robot orientation
Conclusions and Future Work
Notes: Traversability in rough terrain
Contra partially overcome with control limiting approach:
No more assumptions about Acceleration and velocity.
But: Still worst case for orientation (edge approach angle; tipping direction)

## Slide 36: Future Work
Reduce assumptions about robot movement
  Consider robot orientation
  3D grid graph
Slippage
Conclusions and Future Work
x
y
orientation

## Slide 37: Thank you for your attention! Ready for questions
References:
[Chen, 2017] | Chen, Y. F., Everett, M., Liu, M., and How, J. P. Socially aware motion planning with deep reinforcement learning. In: 2017 IEEE/RSJ International Conference on Intelligent Robots and Systems (IROS). IEEE. 2017, pp. 1343–1350.
[Ortiz, 2018] | Ortiz, L. E., Cabrera, V. E., and Goncalves, L. M. Depth data error modeling of the ZED 3D vision sensor from stereolabs. In: ELCVIA: electronic letters on computer vision and image analysis 17(1):1–15, 2018.
[Quigley, 2009] | Quigley, M., Conley, K., Gerkey, B., Faust, J., Foote, T., Leibs, J., Wheeler, R., Ng, A. Y., et al. ROS: an open-source Robot Operating System. In: ICRA workshop on open source software. Vol. 3. 3.2. Kobe, Japan. 2009, p. 5.
[Fankhauser, 2016] | Fankhauser, P. and Hutter, M. A Universal Grid Map Library: Implementation and Use Case for Rough Terrain Navigation. In: Robot Operating System (ROS) – The Complete Reference (Volume 1). Ed. by A. Koubaa. Springer, 2016. Chap. 5.
[Fankhauser, 2018] | Fankhauser, P., Bloesch, M., and Hutter, M. Probabilistic Terrain Mapping for Mobile Robots with Uncertain Localization. In: IEEE Robotics and Automation Letters (RA-L) 3(4):3019–3026, 2018.
[Brooks, 1991] | Brooks, R. A. New approaches to robotics. In: Science 253(5025):1227–1232, 1991.
[Nguyen, 2021] | Nguyen, N. T., Schilling, L., Angern, M. S., Hamann, H., Ernst, F., and Schildbach, G. B-spline path planner for safe navigation of mobile robots. In: 2021 IEEE/RSJ International Conference on Intelligent Robots and Systems (IROS). IEEE. 2021, pp. 339–345.
[Grisetti, 2007] | Grisetti, G., Stachniss, C., and Burgard, W. Improved techniques for grid mapping with rao-blackwellized particle filters. In: IEEE transactions on Robotics 23(1):34–46, 2007.